1.0. WHAT IS OPENGFX?	1

Chapter 1
# Introduction
OpenGFX is an open-source, community-driven graphics API and runtime framework built for modern graphics programming. It emphasizes performance, portability, and hardware longevity, while offering a clean and predictable execution model.
Unlike traditional APIs such as OpenGL or Vulkan, which are merely specifications implemented by hardware vendors, OpenGFX includes an official, reference-grade implementation. This canonical implementation is developed and maintained openly by the OpenGFX community, ensuring consistency across platforms and full transparency of internal behavior. While hardware vendors are free to create their own conformant implementations, the existence of a standard, open reference backend sets OpenGFX apart from legacy APIs.
Designed with modern systems programming in mind, OpenGFX integrates seamlessly with languages that support foreign memory access and memory-safe abstractions, like Java (via Project Panama). Its architecture favors explicit memory management and stateless draw calls, aligning it closer to the Vulkan philosophy while remaining far more accessible and concise.
OpenGFX provides a stable foundation for building low-level rendering applications, graphics engines, and experimental backends, all while freeing developers from vendor lock-in and forced hardware obsolescence.

TODO: INTERNAL ARCHITECTURE
1.1. COMMAND LIST	2
# VIEWPORT AND CANVAS

void glViewport(short width, short height)
Description:
This function accepts two arguments: width and height. It configures the rendering area of OpenGFX.
Parameters:
- width: The viewport width.
- height: The viewport height
API Note: The method glViewport(short x, short y, short width, short height) was deprecated because viewport offsets are not supported anymore. They were considered useless.

void glClear(int rgb)
Description:
This function accepts one argument, the clear color. It fills the canvas with the specified color.
Parameters:
rgb: A 24-bit RGB color.
Behavior:
All the pixels in the framebuffer must be mapped to the same RGB value.
1.1. COMMAND LIST	3
# STATE CONFIGURATION

void glAngleUnit(GLAngleUnit unit)
Description:
Sets the default angle measurement unit for every angle-related function.
Behavior:
Next time you invoke any command related to angles, the default measurement unit will be the specified by the user.
- GLAngleUnit.GL_DEGREES — 360º is an entire rotation.
- GLAngleUnit.GL_RADIANS — 2π radians is an entire rotation.
- GLAngleUnit.GL_NORMALIZED — The value 1 is an entire rotation.

void glInit()
Description:
Initializes OpenGFX.
Behavior:
Undefined. May change depending on the implementor.
Returns:
- true: If OpenGFX was initialized correctly.
- false: If OpenGFX failed during the initialization.

1.1. COMMAND LIST	4
# MATRIX MANIPULATION

void glMatrixMode(GLMatrixMode matrixMode)
Description:
Selects which matrix is going to be affected when calling matrix manipulation methods (e.g.: translations, scales, rotations, ...) that don't accept a GLMatrixMode as an argument.
Behavior:
Copies the matrix's pointer correspondent to the specified matrixMode to a mutable variable. This mutable variable will be normally named matrix (or activeMatrix) and it indicates which matrix must be affected when calling matrix manipulation methods that don't accept a GLMatrixMode as an argument. This doesn't copy memory, just pointers.
Default value:
The default value for this method is: GLMatrixMode.GL_MODEL

void glTranslate(float x, float y, float z)
Description:
Applies a translation to the current matrix.
Behavior:

This translation matrix is multiplied to the active matrix. Whereas M is the value of the active matrix previous to the translation. And (tx, ty and tz) represent a vector.

void glScaleXYZ(float scalar)
Description:
Scales all the components of the current matrix by a factor specified by the parameter scalar.
Behavior:

The current matrix is multiplied by this scaling matrix. Whereas M is the value of the active matrix and f is the scaling factor.

1.1. COMMAND LIST	5

void glScalef(float x, float y, float z)
Description:
Scales all the current matrix components individually by a factor indicated by the parameter correspondant to the coordinate.
Behavior:

Multiplies the active matrix by this scaling matrix. The values x, y and z represent its respective parameter.

void glLoadMatrix(GLMatrixMode matrixMode, float[16] matrix)
Description:
Loads a custom matrix with a specified mode. It's completely independent to any value given to the command glMatrixMode().

1.1. COMMAND LIST	6
# MESH MANIPULATION

void glCreateIndices(GLMesh mesh)
Description:
Instances a placeholder for the indices attribute in the mesh looping through the vertices without altering its order.

1.1. COMMAND LIST	7
# VERTEX DRAWING

void glVertexPointer(int count, ValueLayout type, int stride, MemorySegment pointer)
Description:
Specifies the pointer where the vertices are located. These might be
copied to the GPU if hardware-acceleration is enabled.
Parameters:
- count: The dimension of the vertex. Allowed values are: 1, 2, 3 and 4. Any value other than those is going to trigger a GLError.GL_INVALID_VALUE.
- type: The type of the vertices. Allowed: ValueLayout.JAVA_INT and all of its members.
- stride: The byte offset between consecutive vertex attributes. If zero, the data is tightly packed.
- pointer: A MemorySegment pointing to the start of the vertex buffer data.
Behavior:
The specified vertex buffer becomes active immediately and is used in subsequent draw calls. If pointer is MemorySegment.NULL, the current vertex pointer is cleared.